The Migration of E-Tag 1.7.095 from NERC Policies                                      to the NERC Reliability Functional Model, Version 2

The Interchange Subcommittee requested the Transaction Information System Working Group (TISWG) identify changes to the E-Tag Functional Specification required to enable Version 0 standards.  Version 0 standards will translate current NERC policies in NERC Reliability Functional Model language and a corresponding translation of the NERC Functional Specification.  One goal of the TISWG is to minimize changes to the E-Tag Specification and associated company’s backend systems.

# Aligning E-Tagging with the Functional Model

The TISWG compared the Functional Model functions with the current E-Tagging entities and found the following:

- Six E-Tag entities have a one-to-one correlation with Functional Model functions (See Table 1).

### Table 1

| NERC Reliability Functional Model | E-Tag 1.7.095 Entities |
| --- | --- |
| Reliability Authority | 1. Reliability Coordinator (RC) 2. Interchange Distribution Calculator (IDC) |
| Balancing Authority | 1. Control Area (CA) 2. Scheduling Entity (SE) |
| Market Operator (or Resource Dispatcher) | Control Area (CA) |
| Transmission Service Provider | Transmission Provider (TP) |
| Purchasing-Selling Entity | 1. Purchasing- Selling Entity (PSE) 2. Generation Providing Entity (GPE) 3. Transmission Customer (TC) |
| Load-Serving Entity | 1. Load Serving Entity (LSE) 2. Transmission Customer (TC) |

Industry agreement on the relationships in Table 1 will minimize the changes to existing company backend systems and tools.

- Two functions, the Transmission Planner and the Planning Authority did not exist in E-Tagging and therefore no alignment was necessary.

- Table 2 provides a listing of the current NERC reliability functions and the associated Reliability Model’s Responsible Entities. The table lists the corresponding page number where this information can be located in the Functional Model.

## Table 2

| Reliability Functions | Responsible Entity | Page |
| --- | --- | --- |
| Operating Reliability | Reliability Authority | 12 |
| Planning Reliability | Planning Authority | 15 |
| Balancing | Balancing Authority | 19 |
| Market Operations | Market Operator (or Resource Dispatcher) | 22 |
| Resource Planning | Resource Planner | 24 |
| Transmission Operations | Transmission Operator | 26 |
| Interchange | Interchange Authority | 29 |
| Transmission Planning | Transmission Planner | 32 |
| Transmission Service | Transmission Service Provider | 35 |
| Transmission Ownership | Transmission Owner | 37 |
| Distribution | Distribution Provider | 39 |
| Generator Operation | Generator Operator | 41 |
| Generator Ownership | Generator Owner | 43 |
| Purchasing-Selling | Purchasing-Selling Entity | 45 |
| Load-Serving | Load-Serving Entity | 47 |
| Compliance Monitoring | Compliance Monitor | 49 |
| Standards Development | Standards Developer | 51 |

# Interchange Authority Function

The TISWG made the assumption that the Interchange Authority (IA) function will not be part of the Version 0 standards.  Instead, the intent is to maintain the current interchange scheduling approach as currently being performed by Generating Control Areas and Load Control Areas.

Describing the Reliability Authority

The Function Model allows approval rights for the Reliability Authority on bilateral schedules from a reliability perspective. The current E-Tag specification does not allow the Reliability Coordinator these same rights; therefore, for Version 0 standards the TISWG assumes that the Reliability Authority will not be allowed these approval rights, but rather be copied on all implemented E-Tags as it is done today.

# Footnotes

See Describing the Reliability Authority section of this paper.