1.  RECOMMENDED ACTION:	EFFECT OF EC VOTE TO ACCEPT RECOMMENDED ACTION:

|  | Accept as requested |  | Change to Existing Practice |
| --- | --- | --- | --- |
|  | Accept as modified below |  | Status Quo |
|  | Decline |  |  |

2.  TYPE OF DEVELOPMENT/MAINTENANCE

| Per Request: | Per Recommendation: |
| --- | --- |
|  | Initiation |  | Initiation |
|  | Modification |  | Modification |
|  | Interpretation |  | Interpretation |
|  | Withdrawal |  | Withdrawal |
|  | Principle |  | Principle |
|  | Definition |  | Definition |
|  | Business Practice Standard |  | Business Practice Standard |
|  | Document |  | Document |
|  | Data Element |  | Data Element |
|  | Code Value |  | Code Value |
|  | X12 Implementation Guide |  | X12 Implementation Guide |
|  | Business Process Documentation |  | Business Process Documentation |

3.  RECOMMENDATION

SUMMARY:

Recommended Standards:

4.  SUPPORTING DOCUMENTATION

a.  Description of Request:

On September 30, 2009 the National Institute of Standards and Technology officially assigned NAESB the responsibility to develop Requirements and Use Cases pertinent to Priority Action Plan items 3, 4 and 9. A complete description of each item is available on the NIST Web site located at http://collaborate.nist.gov/twiki-sggrid/bin/view/_SmartGridInterimRoadmap/PriorityActionPlans

This recommendation specifically pertains to PAP 04, “A Common Scheduling Mechanism for Energy Transactions”.

b.  Description of Recommendation:

This recommendation contains a set of requirements relating to the use of date and time based data elements that are used in transactions for Demand Response Programs. This information is being provided to NIST in order to aid in the development of a standard representation for date/time based data elements, possibly an XML representation of ICalendar.

Although there are many other areas where date/time based data elements are used in energy industry transactions this recommendation is limited in scope to only those date/time based data elements that are utilized in  Demand Response Programs.

## Date and Time Based Data Elements Utilized in Demand Response Programs

| Data Element Name | Description |
| --- | --- |
| Adjustment Window | The period of time prior to a Demand Response Event used for calculating a Baseline Adjustment. |
| Advance Notification | One or more communications to Demand Resources of an impending Demand Response Event in advance of the actual event. |
| Baseline Window | The window of time preceding and optionally following, a Demand Response Event over which the electricity consumption data is collected for the purpose of establishing a Baseline. |
| Demand Response Event | The time periods, deadlines and transitions during which Demand Resources perform. The Program Administrator should specify the duration and applicability of a Demand Response Event. All deadlines, time periods and transitions may not be applicable to all Demand Response products or services. |
| Deployment | The time at which a Demand Resource begins reducing Demand on the system in response to an instruction. |
| Deployment Period | The time in a Demand Response Event beginning with the Deployment and ending with the Release/Recall |
| Meter Data Recording Interval | The time between electricity meter consumption recordings |
| Meter Data Reporting Deadline | The maximum allowed time from the end of a Demand Response Event (Normal Operations) to the time when meter data is required to be submitted for performance evaluation and settlement. The Meter Data Reporting Deadline may be either relative (a number of hours/days after Normal Operations) or fixed (a fixed calendar time, such as end-of-month). |
| Performance Window | The period of time in a Demand Response Event analyzed by the Program Administrator to measure and verify the Demand Reduction Value for a Demand Resource. |
| Ramp Period | The time between Deployment and Reduction Deadline, representing the period of time over which a Demand Resource is expected to achieve its change in Demand |
| Recovery Period | The time between Release/Recall and Normal Operations, representing the window over which Demand Resources are required to return to their normal Load. |
| Reduction Deadline | The time at the end of the Ramp Period when a Demand Resource is required to have met its Demand Reduction Value obligation |
| Release/Recall | The time when a Program Administrator notifies a Demand Resource that the Deployment Period has ended or will end |
| Sustained Response Period | The time between Reduction Deadline and Release/Recall, representing the window over which a Demand Resource is required to maintain its reduced net consumption of electricity |
| Telemetry Interval | The time unit between communications between a Demand Resource or Demand Response Provider and a Program Administrator |

## Requirements for Date and Time Usage

Demand Response Programs employ a combination of absolute dates/times, absolute periods (range) of dates/times, relative dates/times, recurring dates/times, absolute intervals and absolute durations in order to communicate temporal information pertaining to demand response transactions. Demand Response Programs must also accommodate time zone variations, leap years and leap seconds and the use of daylight savings time. Any calendaring/scheduling standard that is applicable to Demand Responsde programs must be capable of supporting this range of requirements.  An incomplete, but representative, set of examples is provided below:

| Type of Representation | Data Element | Usage Examples |
| --- | --- | --- |
| Absolute date/time | Effective start date Effective start date and time | 2009-11-01 2009-11-01T01:00:00-Z |
| Absolute Periods (range) | Deployment Period | 2009-11-01T01:00:00-Z/2009-11-02T24:00:00-Z |
| Relative date/time (time-point) | Reduction Deadline | 30 minutes from a specified point in time |
| Recurring date/time | Market Closing | Every day at 12:00 noon |
| Absolute Interval | Meter Data Recording Interval System Frequency | Every 5 minutes 60 cycles per second |
| Absolute Duration | Outage Duration Minimum Run Time | 2 days 4 hours |

c.  Business Purpose:

This recommendation has been developed in response to a request from NIST to provide use cases and requirements germane to the use of dates/times within a broad spectrum of energy transactions. The scope of this effort has been limited to Demand Response Programs in order to meet NIST’s deadline for this effort.

d.  Commentary/Rationale of Subcommittee(s)/Task Force(s):

# Footnotes

http://collaborate.nist.gov/twiki-sggrid/bin/view/SmartGrid/PAP04Schedules

http://tools.ietf.org/html/rfc5545