## Slide 1: NAESB GEH Forum Dan Buckner Director of Fuels Origination and Strategic Development

## Slide 2: Who is ACES
ACES is a Nationwide Energy Management Company
We Help Our Clients Buy, Sell, and Manage Energy More Efficiently, With Less Risk

## Slide 3: ACES Today
Portfolio Management Overview
  Manage Resources in PJM, MISO, SPP, CAISO, ERCOT
  50,000 MW of Generation From 300 Plants
  50,000 MW of Load
  3.0 Bcf/Day Peak Natural Gas
  Active on 30 Natural Gas Pipelines
Four Regional Trading Centers:
  Indiana, Minnesota, North Carolina, & Arizona

## Slide 4: ACES Today
RTC
Customers
Members
Inactive Customers
Customer Load
Member Load
Inactive Customer Load

## Slide 5: Review: FERC Activity
March 2014: FERC Issues NOPR
  “To Better Coordinate the Scheduling of Natural Gas and Electricity Markets in Light of Increased Reliance on Natural Gas For Electric Generation”
April 2015: FERC Issues Final Rule
  Later Deadline For Timely Nomination Cycle
  Adds 1 Additional Intraday Nomination Cycle
  No Change to the Gas Day Start Time (10 a.m. EPT)
  ISOs/RTOs Required to Align Their DA and RAC/RUC Unit Commitment Schedules in Advance of the Timely and Evening Cycles; or Show Cause
Source: FERC Gas Day Final Rule (Order No. 809)

## Slide 6: Natural Gas Timeline Changes
Natural Gas Scheduling Timeline (EPT) |  | Current Times | Revised Times
Timely Nomination Cycle | Deadline | 12:30 p.m. | 2:00 p.m.
 | Gas Flow Begins | 10:00 a.m. | 10:00 a.m.
Evening Nomination Cycle | Deadline | 7:00 p.m. | 7:00 p.m.
 | Gas Flow Begins | 10:00 a.m. | 10:00 a.m.
Intraday 1 Nomination Cycle | Deadline | 11:00 a.m. | 11:00 a.m.
 | Gas Flow Begins | 6:00 p.m. | 3:00 p.m.
 | IT Bump Rights | Yes | Yes
Intraday 2 Nomination Cycle | Deadline | 6:00 p.m. | 3:30 p.m.
 | Gas Flow Begins | 10:00 p.m. | 7:00 p.m.
 | IT Bump Rights | No | Yes
Intraday 3 Nomination Cycle | Deadline |  | 8:00 p.m.
 | Gas Flow Begins |  | 11:00 p.m.
 | IT Bump Rights |  | No
Source: FERC Gas Day Final Rule (Order No. 809)

## Slide 7: Day-Ahead Timelines
Processing Times For DA Energy Markets Are Different Across Markets, Driving the Different Timelines
Effective Date Refers to DA Timeline Changes
  Not Electric Operating Day
FERC Has Yet to Rule on MISO’s Proposed Effective Date
SPP May Need to Clarify With FERC Regarding the Effective Date
RTO | Effective Date* | Old DA Submittal | New DA Submittal | Old DA Results | New DA Results
PJM | 3/31/16 | 12:00 p.m. EPT | 10:30 a.m. EPT | 4:00 p.m. EPT | 1:30 p.m. EPT
MISO | 11/5/16* | 11:00 a.m. EST | 10:30 a.m. EPT | 3:00 p.m. EST | 1:30 p.m. EPT
SPP | 10/1/16* | 12:00 p.m. EPT | 10:30 a.m. EPT | 5:00 p.m. EPT | 3:00 p.m. EPT

## Slide 8: PJM (All Times EPT)
RTO | Effective Date | Gas Trading | DA Bids | DA Awards | Timely Cycle
PJM | 3/31/16 | 8:00 – 10:00 a.m.* | 10:30 a.m. | 1:30 p.m.* | 2:00 p.m.
Will Gas Markets Change?
  Tight Execution Window
  Services, Trading Window, Etc.
Purchase Gas For DA Award in Timely Cycle?
  Peak Days - May Help With Priority on Pipeline?
  DA Award is Not Necessarily an RT Dispatch, Could Impact Strategy
RTO | Rebid Period | RAC Results | Nomination Cycle
PJM | 1:30 – 2:15 p.m. (Opening as Early as Awards Post) | 3:00 p.m. For Morning Ramp CTs | 3:30 p.m. (ID2)
 |  | 6:30 p.m. For Other Plants | 7:00 p.m. (Evening)
RAC Dispatch in PJM is Treated as a RT Dispatch
  Designed to Allow For Gas Purchases During Evening Cycle
  Definitive Start Time, But Not Definitive Gas Volumes
  Tight Execution Window and Market Illiquidity

## Slide 9: Scheduling Request
Why Are We Here?
  We request that gas and electric industries, through NAESB, explore the potential for faster, computerized scheduling when shippers and confirming parties all submit electronic nominations and confirmations, including a streamlined confirmation process, if necessary.
Coordination/Timing Challenges Still Exist
Would a Quicker Nominations Process be an Improvement?

## Slide 10
Coordination Challenges

## Slide 11: Generation Profile Challenge
Source: ACES

## Slide 12: Timing Challenges
Generator Schedule Does not Match Gas Cycle
Generator Schedule Provided After Nomination Cycle Deadline
Can Quicker Electronic Scheduling Improve Coordination Between These Markets?
Source: ACES

## Slide 13: Generator Requirements
Even Shippers With FT Depend on Interruptible Operational Flexibility From the Pipelines to Manage Key Operational Requirements
Generator Needs | Firm Transportation Service
Quick Start Up Capability | Not a Firm Right
Non-Uniform Hourly Consumption | Not a Firm Right
Pressure Requirements | Sometimes Included
After Hours Consumption Change Capability | Not a Firm Right

## Slide 14: Generator Requirements
Unfortunately, Pipelines Have a Limited Amount of No-Notice Services Available
Generator Needs | Firm No-Notice Services
Quick Start Up Capability | Firm
Non-Uniform Hourly Consumption | Typically Allowed
Pressure Requirements | Sometimes Included
After Hours Consumption Change Capability | Firm

## Slide 15: Interruptible Services
MISO Winter Generator Fuel Survey (Dec 2015)
  13% of Generators Relied on FT Only
Source: MISO

## Slide 16: Interruptible Services
PJM Gas-Fired Generation (2014 EIPC Study)
  60% Do Not Have FT or Dual Fuel (Rely on IT)
  25% Have Dual Fuel
  15% Have FT
PJM’s Capacity Performance
  Provides Some Recovery of Pipeline Costs
    $ Amount Determined by Auction
    Cleared 1 Year at a Time – Pipeline Expansion Projects Require Multiyear Service Agreements/Cost Recovery

## Slide 17: Interruptible Flexibility
Power Generators Rely on This Interruptible Operational Flexibility
  For Quick Starts
  For Non-Uniform Hourly Consumption
  To Allow for Changes After Hours
On Many Pipelines, These Services Have Been Highly Reliable
Forcing Pipelines to Process Quicker May Result in Decreased Operational Flexibility

## Slide 18: Impacts of Quicker Scheduling
Quicker Scheduling MIGHT Provide Increased Operational Flexibility
  Better Coordination with Dispatch Timing
Quicker Scheduling MIGHT Reduce Operational Flexibility
  Less Time to Determine if Interruptible Operational Flexibility is Available
Limited Firm Services Available to Provide the Required Operational Flexibility
  Electric Generators Cannot Lose This Operational Flexibility

## Slide 19: Summary
Coordination/Timing Challenges Remain
Generators Rely on Interruptible Services
  Firm Transportation Does not Provide Sufficient Operational Flexibility
  No-Notice Services are Limited and Expensive
Gaining Quicker Electronic Coordination, But Losing the Interruptible Operational Flexibility Would Impact Reliability
Proceed with Caution