NAESB Electronic Tagging (e-Tag) Specification Version 1.8.2 Implementation Plan

Description of change(s):

Please see the document created by the NAESB Wholesale Electric Quadrant (WEQ) Coordinate Interchange Scheduling Subcommittee (CISS) available at the following link:

Implementation:

Single stage approach, based on creation time:

1.8.2 Implementation Date: March 31, 2015 00:00 CST (Midnight between March 30 and March 31 2015)

1.8.1.1 Retirement Date: May 1, 2015 00:00 CST (Midnight between April 30 and May 1, 2015)

Vendors will implement the new e-Tag version at the Implementation Date. E-Tags created prior to the cut-over will be older version e-Tags and will work as they do today. E-Tags created at and after the cut-over will be newer version e-Tags and will behave as per the 1.8.2 changes (with regards to profile calculation, NITS resource capability, new validations, etc.).

If there is a need to roll back, a decision must be made within 30 minutes, and the roll back must be complete no later than one hour after the Implementation Date. In the event of a roll back, the e-Tags created after the cut-over, up to the point of roll back must be terminated. E-Tag Vendors shall configure their authority services to automatically terminate any outstanding 1.8.2 e-Tags.

With a successful transition to e-Tag 1.8.2, all remaining 1.8.1.1 tags should be terminated, and a new 1.8.2 version of the tag created by no later than the 1.8.1.1 Retirement Date. Vendors will work with end users to provide the ability to determine which tags are using the Version 1.8.1.1 of the e-Tag Specification. Visibility of the tag version should be available on the first day after implementation. Tag Authors will be responsible for recreating the tags. Recreation of the tags may be made at any time between the 1.8.2 Implementation Date and the 1.8.1.1 Retirement Date.

E-Tag vendors shall configure the Authority Services to automatically terminate any outstanding e-Tags using the 1.8.1.1 Specification on 1.8.1.1 Retirement Date. This termination shall be entered seven days prior to the retirement date to ensure customers are provided ample notice. Outstanding 1.8.1.1 e-Tags will receive termination request with a comment on the tag that the termination is due to the retiring 1.8.1.1 specification. The specific verbiage of the comment field should be as follows:

This tag is using 1.8.1.1. It will be terminated on May 1, 2015 at 00:00 CST. Please create a new tag if needed.

NOTE:  This occurs on May 1, 2015 00:00 CST. All 1.8.1.1 tags ending after the times below will automatically be terminated.

Atlantic Daylight Time 			May 1, 2015	03:00

Eastern Daylight Time 			May 1, 2015	02:00

Central Daylight Time			May 1, 2015	01:00

Mountain Daylight Time			May 1, 2015	00:00

Pacific Daylight Time			April 30, 2015	23:00